## Slide 1
Copyright© Eclipse Foundation AISBL and contributors. Made available under CC-BY-SA 4.0 International.
Real Hardware · What We Built
Built
Proven live
✓ AZ3166 · ThreadX · temp + humidity
✓ S32K148 · OpenBSW · own UDS DID
✓ Guardian in AutoSD VM · Pi 5
✓ Guardian → RPC → DoIP → LED
✓ Dashboard · manual window control
→ 31 °C + child + HVAC fault
→ Window 25 % · read back via DoIP
→ LED blinks while window is open
→ Reset to 0 % from the dashboard
→ guardian.rs · 0 hardware lines
Notes: (~40 s) What we brought up on real hardware. A real AZ3166 board running Eclipse ThreadX measures temperature and humidity. A real NXP S32K148 running Eclipse OpenBSW is the window controller, with our own WindowPosition data identifier added to the firmware. The Guardian runs unchanged in an AutoSD VM on a Raspberry Pi 5. Proven live on the bench: at 31 degrees with a child present and an HVAC fault, the Guardian sent one RPC, the window went to 25 percent over UDS on DoIP, we read the value back from the board, and its LED blinks while the window is open. The dashboard can open and reset the window by hand. None of this touched guardian.rs.